## Slide 1: Digital Logic Design
Semester II
FY
Course Code
316U06C203
Jan – May 2026

## Slide 2: Logic Representation and Minimization Techniques

## Slide 3: Contents
Basic gates AND, OR, NOT
Derived gates : NAND, NOR, XOR,
Boolean Theorems
Representation of Logic in Boolean Equation
SOP and POS form
Minimization of Boolean equation using Algebra
Minimization using K Map

## Slide 4: Basic Gates
Gate Name | Symbol | Truth Table
AND |  | 
OR |  | 
NOT |  | 
A | B | Y
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
A | A’
0 | 1
1 | 0

## Slide 5: Derived Gates
Gate Name | Symbol | Truth Table
NAND |  | 
NOR |  | 
XOR |  | 
A | B | Y
0 | 0 | 1
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A | B | Y
0 | 0 | 1
0 | 1 | 0
1 | 0 | 0
1 | 1 | 0
A | B | Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 6: Boolean Algebra Theorems
Identity Laws
A + 0 = A A · 1 = A
2. Null/Annihilation Laws
A + 1 = 1 A · 0 = 0
3. Idempotent Laws
A + A = A A · A = A
4. Complement Laws
A + A′ = 1 A · A′ = 0
5. Double Negation Law
(A′)′ = A
6. Commutative Laws
A + B = B + A A · B = B · A

## Slide 7: Boolean Algebra Theorems..
7. Associative Laws
(A + B) + C = A + (B + C) (A · B) · C = A · (B · C)
8. Distributive Laws
A · (B + C) = A·B + A·C A + (B · C) = (A + B) · (A + C)
9. Absorption Laws
A + A·B = A A · (A + B) = A
10. DeMorgan’s Theorems
(A · B)′ = A′ + B′ (A + B)′ = A′ · B′
11. Redundancy Laws
A + A′·B = A + B A · (A′ + B) = A·B

## Slide 8: Simplification using Boolean Theorems
Given an Boolean Expression check whether it is optimized
Y = AB+ AB’C+C’+ABC
Circuit requires 2 i/p AND 5 no, NOT 2 No,
2 i/p OR 3 No
Y = AB+ AB’C+C’+ABC +ABC ……A+A =A
= AB + ABC+ AB’C+C’+ABC...commutative
= AB ( 1+C) + AB’C+C’+ABC …. Distributive
= AB + AB’C+ABC+ C’…. 1+A = 1
= AB+ AC(B’+B)+C’ ….. Distributive
= AB + AC + C’
= AB + A+C’ = A(B+1) +C’ = A+C’
A | B | C | Y
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
Y = A’B’C’+ A’BC’+AB’C’+AB’C+ABC’+ABC

## Slide 9: Simplify
F (A, B, C, D) = (A + B’).(ACB + B’.[C + A]) + ABC’.(A’B + A)
Identify how many inputs...D not required
Always maintain their sequence ( even if it does not matter )
F = (A+B’) . ( ABC+B’C+AB’) + ( AA’BBC’ + AABC’)
= (AABC+AB’C+AAB’+ABB’C+B’B’C+AB’B’) + (AA’BBC’ + AABC’)
= ABC+AB’C+AB’+0+B’C+AB’ +0+ABC’
= ABC+AB’(C+1)+B’C+AB’+ABC’
= AB(C+C’) +AB’ +B’C
= AB+ AB’+B’C
= A(B+B’) + B’C
=A+B’C

## Slide 10: Representation of Logic using Boolean Expression
Write a truth table for function which is one when the four digit number is prime number
No of Inputs?
Truth Table
Minterns
Maxterms
Output expressed as a function of inputs
= sum of minterms = sum of Products = SOP
= Product of Maxterms =Product of Sums

## Slide 11: Boolean Expression
Prime = 1 when input is
2,3,5,7,11,13
Choose rows of truth table having output 1
Look at inputs in that row
Write an expression for the row as product ( AND )
If variable is having value zero write its complement, if it is having value 1 write the variable as it is
A | B | C | D | Prime
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0
P = A’B’CD’+ A’B’CD+
A’BC’D + A’BCD+
AB’CD + ABC’D
= A’B’C+ A’BD +
AB’CD +ABC’D

## Slide 12: Representation of Logic in SOP and POS form
In any Truth Table Output Values are either zero / one
Minterms are used to represent the logic expression for output = 1.
A minterm is a product (AND) of all input variables in either true or complemented form, such that only one combination results in 1.
Maxterms are used to represent the logic expression for output = 0.
A maxterm is a sum (OR) of all input variables in either true or complemented form, such that only one combination results in 0.

## Slide 13: Representation of Logic in SOP and POS form
Any Truth Table can be represented as
  Sum of Products ( Minterms)
  Product of Sums( Maxterms)
  P = m2+m3+m5+ m7+ m11+m13 ( SOP)
  P = M0. M1. M4. M6. M8. M9. M10. M12. M14. M15 ( POS)
  Minterms are represented as Products
  m2 = A’B’CD’, m3= A’B’CD m11 = AB’CD etc
  Maxterms are represented as Sums
  M0 = A+B+C+D, M1 = A+B+C+D’ , M6 = A+B’+C’+D
  M12 = A’+B’+C+D M15 = A’+B’+C’+D’ etc

## Slide 14: Representation of Logic in SOP and POS form
SOP form of boolean expression can also be written as
P = ∑ m(2,3,5,7,11,13) …SOP
POS form as
P = π M( 0,1,4,6,8,9,10,12,14,15) …POS
Total terms ( rows of the truth table) are dependent on number of inputs
For n inputs terms = 2**n

## Slide 15: Representation of Logic in SOP and POS form
SOP form of boolean expression can also be written as
P = ∑ m(2,3,5,7,11,13) …SOP
POS form as
P = π M( 0,1,4,6,8,9,10,12,14,15) …POS
Total terms ( rows of the truth table) are dependent on number of inputs
For n inputs terms = 2**n
SOP (Sum of Products) | POS (Product of Sums)
Minterms (Output = 1) | Maxterms (Output = 0)
OR of ANDs (e.g., A·B + C) | AND of ORs (e.g., (A + B)·(C + D))
Logic implementation via AND-OR networks | Logic implementation via OR-AND networks

## Slide 16: Representation of Logic in SOP and POS form
Consider function Y( A,B,C,D) = ∑ m(2,3,5,7,8,10,11,13) …SOP
Y = A’B’CD’+A’B’CD +A’BC’D+A’BCD +AB’C’D’+AB’CD’+AB’CD+ABC’D
= A’B’CD’+A’B’CD +A’BC’D+A’BCD +AB’C’D’+AB’CD’+AB’CD+ABC’D
= A’B’C(D’+D ) + A’BD ( C’+C) + AB’ D’ (C’+C) +AB’CD+ABC’D
= A’B’C + A’BD+AB’D+AB’CD + ABC’D
=B’C(A’+AD) +A’BD +AD(B’+BC’) …………A’+AD = A’+D, B’+BC’ = B’+C’
= B’C(A’+D) + A’BD+ AD(B’+C’)
= A’B’C+B’CD+A’BD +AB’D+AC’D

## Slide 17: Representation of Expression in Karnaugh Maps
Consider function Y( A,B,C) = ∑ m(1,2,3,4,7,) …SOP
Y = A’B’C+A’BC’+A’BC+AB’C’+ABC = A’C(B’+B)+A’B(C+C’)+BC(A’+A) +AB’C’
= A’C+A’B+BC+AB’C’
A’C+A’B+BC+AB’C’
AB/C | 00 | 01 | 11 | 10
0 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0

## Slide 18: Minimization using Karnaugh Maps
Consider function Y( A,B,C,D) = ∑ m(1,2,3,4,7,8,11,13,15) …SOP
A’B’D + A’B’C + CD + ABD + A’BC’D’ + AB’C’D’
AB/CD | 00 | 01 | 11 | 10
00 | 0 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 1 | 1 | 1 | 1
10 | 1 | 0 | 0 | 0

## Slide 19: Karnaugh Maps Minimization Rules
Identify all minterns in the given funtion. ( or maxterms)
Group adjacent minterms for SOP ( maxterms for POS)
Groups having 1,2,4,8…upto 2**n for n variable K Map
K-maps are cylindrical: the left and right edges are adjacent, as are the top and bottom. This allows wrap-around groupings.
A cell can be part of multiple groups if it helps make larger groups.
Make Largest Possible Groups First
All minterms must be covered even if it is a group of 1 term
Make sure that no group is redundant ( redundant group is the one in which all minterms are part of some other group)
For each group:
Eliminate the variables that change within the group.
Keep variables that are the same for all cells in the group.
To represent each group consider a product with variable (for 1) and
its complement (for 0) for SOP

## Slide 20: Minimization using Karnaugh Maps
Consider function Y( A,B,C,D) = ∑ m(0,1,2,3,4,6,7,8,11,13,15) …SOP
A’B’ + A’D’ + CD + ABD + B’C’D’
AB/CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 0 | 0

## Slide 21: Karnaugh Maps with Don’t care terms:
Consider function Y( A,B,C,D) = ∑ m(0,1,2,4,6,11,15) + d(3,9,13)…SOP
Y = A’D’+A’B’C’+ACD …without considering don’t care terms
Y = A’D’+A’B’+AD …with Don’t cares
AB/CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 0
01 | 1 | 0 | X | X
11 | X | 0 | 1 | 1
10 | 1 | 1 | 0 | 0
AB/CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 0
01 | 1 | 0 | X | X
11 | X | 0 | 1 | 1
10 | 1 | 1 | 0 | 0

## Slide 22: Minimization using Karnaugh Maps (POS)
Consider function Y( A,B,C,D) = ∑ m(0,1,2,3,4,6,7,8,11,13,15) …SOP
= π M(5,9,10,12,14) …POS
Y=(A+B’+C+D’).(A’+B+C+D’).(A’+B’+D).(A’+C’+D)
A’B’ + A’D’ + CD + ABD + B’C’D’
AB/CD | 00 | 01 | 11 | 10
00 | 1 | 1 | 0 | 1
01 | 1 | 0 | 1 | 0
11 | 1 | 1 | 1 | 1
10 | 1 | 1 | 0 | 0

## Slide 23: Minimization using Karnaugh Maps
F(A,B,C,D) = Σ m(0, 2, 4, 5, 8, 10, 12, 14, 15)
F(A,B,C,D) = ∑m(0,1,4,5,10,11,13,14,15)
F(A,B,C,D) = πM(0,1,4,5,10,11,13,14,15)
F(A,B,C,D) = π M(0,1,6,7,9,11,12,13,15)
AB/CD | 00 | 01 | 11 | 10
00 |  |  |  | 
01 |  |  |  | 
11 |  |  |  | 
10 |  |  |  |